## Slide 1: Final Project 1

## Slide 2: Part 1: Passive single-harmonic trap HPF
Specifications
  Passband frequency of interest 7.9 GHz w/ 1 GHz BW
  Matching, S11 < -10 dB
  Input/output port impedances: 50/50 Ω
  Insertion loss/NF < 3.5 dB
  In-band ripple <1 dB
  Rejection at 5.8 GHz > 15 dB
  Rejection at 5.1 GHz > 20 dB
Choose the type of filter and order through hand calculations, online calculators (e.g., rfcooltools.com), or look up tables. Build layout (to approximate interconnects) and use Momentum to extract interconnects. Provide reasons for your choices!

## Slide 3: Part 2: Build amplifier/buffer (A) for impedance transformation
HPF
A
Load: 100 Ω
Source: 50 Ω
Zi,A =50 Ω

## Slide 4: Requirements
Presentation in PowerPoint
No screenshots: draw schematic incl. interconnects
  Provide detail (e.g., inductance and capacitance values of the components, length, width, L, C of the interconnects)
Table of specifications and results
Graphs for S21 (dB20 and phase) and S11 (dB20), NF and group delay
Graphs of inductor parameters (e.g., rs, L, Q and SRF) for given dimension