## Slide 1: Address Translation
Tore Larsen
Material developed by: Kai Li, Princeton University

## Slide 2: Topics
Virtual memory
  Virtualization
  Protection
Address translation
  Base and bound
  Segmentation
  Paging
  Translation look-ahead buffer (TLB)

## Slide 3: Issues
Many processes running concurrently
Location transparency
Address space may exceed memory size
  Many small processes whose total size may exceed memory
  Even one large may exceed physical memory size
Address space may be sparsely used
Protection
  OS protected from user processes
  User processes protected from each other

## Slide 4: The Big Picture
Memory is fast
  but expensive
Disks are cheap
  but slow
Goals
  Run programs as efficiently as possible
  Make system as safe as possible

## Slide 5: Strategies
Size: Can we use slow disks to “extend” the size of available memory?
  Disk accesses must be rare in comparison to memory accesses so that each disk access is amortized over many memory accesses
Location: Can we device a mechanism that delays the bindings of program address to memory location? Transparency and flexibility.
Sparsity: Can we avoid reserving memory for non-used regions of address space?
Process protection: Must check access rights for every memory access

## Slide 6: Protection Issue
Errors in one process should not affect other processes
For each process, need to enforce that every load or store are to “legal” regions of memory

## Slide 7: Expansion - Location Transparency Issue
Each process should be able to run regardless of location in memory
Regardless of memory size?
Dynamically relocateable?
Memory fragmentation
  External fragmentation – Among processes
  Internal fragmentation – Within processes
Approach
  Give each process large “fake” address space
  Relocate each memory access to actual memory addres

## Slide 8: Why Virtual Memory?
Use secondary storage
  Extend expensive DRAM with reasonable performance
Provide Protection
  Programs do not step over each other, communicate with each other require explicit IPC operations
Convenience
  Flat address space and programs have the same view of the world
Flexibility
  Processes may be located anywhere in memory, may be moved while executing, may reside partially in memory and partially on disk

## Slide 9: Design Issues
How is memory partitioned?
How are processes (re)located?
How is protection enforced?

## Slide 10: Address Mapping Granularity
Mapping mechanism
  Virtual addresses are mapped to DRAM addresses or onto disk
Mapping granularity?
  Increased granularity
    Increases flexibility
    Decreases internal fragmentation
    Requires more mapping information & Handling
Extremes
  Any byte to any byte: Huge map size
  Whole segments: Large segments cause problems

## Slide 11: Locality of Reference
Behaviors exhibited by most programs
Locality in time
  When an item is addressed, it is likely to be addressed again shortly
Locality in space
  When an item is addressed, its neighboring items are likely to be addressed shortly
Basis of caching
Argues that recently accessed items should be cached together with an encompassing region; A block (or line)
20/80 rule: 20 % of memory gets 80 % of references
Keep the 20 % in memory

## Slide 12: Translation Overview
Actual translation is in hardware (MMU)
Controlled in privileged software
CPU view
  what program sees, virtual memory
Memory & I/O view
  physical memory
Translation
(MMU)
CPU
virtual address
Physical
memory
physical address
I/O
device

## Slide 13: Goals of Translation
Implicit translation for each memory reference
A hit should be very fast
Trigger an exception on a miss
Protected from user’s faults
Registers
Cache(s)
DRAM
Disk
2-20x
100-300x
20M-30Mx
paging

## Slide 14: Base and Bound
Built in Cray-1
Protection
  A program can only access physical memory in [base, base+bound]
On a context switch:
  Save/restore base, bound registers
Pros
  Simple
  Flat
Cons:
  Fragmentation
  Difficult to share
  Difficult to use disks
virtual address
base
bound
error
+
>
physical address

## Slide 15: Segmentation
Provides separate virtual address spaces (segments)
Each process has a table of (seg, size)
Protection
  Each entry has (nil,read,write)
On a context switch
  Save/restore the table or a pointer to the table in kernel memory
Pros
  Efficient
  Easy to share
Cons:
  Complex management
  Fragmentation within a segment
physical address
+
segment
offset
Virtual address
seg
size
.
.
.
>
error

## Slide 16: Paging
Use a fixed size unit called page
Pages not visible from program
Use a page table to translate
Various bits in each entry
Context switch
  Similar to the segmentation scheme
What should be the page size?
Pros
  Simple allocation
  Easy to share
Cons
  Big page tables
  How to deal with holes?
VPage #
offset
Virtual address
.
.
.
>
error
PPage#
...
PPage#
...
...
PPage #
offset
Physical address
Page table
page table size

## Slide 17: How Many PTEs Do We Need?
Assume 4KB page size
  12 bit (low order) displacement within page
  20 bit (high order) page#
Worst case for 32-bit address machine
  # of processes  220
  220 PTEs per page table (~4MBytes). 10K processes?
What about 64-bit address machine?
  # of processes  252
  Page table won’t fit on disk (252 PTEs = 16PBytes)

## Slide 18: Segmentation with Paging
VPage #
offset
Virtual address
.
.
.
>
PPage#
...
PPage#
...
...
PPage #
offset
Physical address
Page table
seg
size
.
.
.
Vseg #
error
Multics was the first system to combine segmentation and paging. www.multicians.org

## Slide 19: Multiple-Level Page Tables
Directory
.
.
.
pte
.
.
.
.
.
.
.
.
.
dir
table
offset
Virtual address

## Slide 20: Inverted Page Tables
Main idea
  One PTE for each physical page frame
  Hash (Vpage, pid) to Ppage#
Pros
  Small page table for large address space
Cons
  Lookup is difficult
  Overhead of managing hash chains, etc
pid
vpage
offset
pid
vpage
0
k
n-1
k
offset
Virtual
address
Physical
address
Inverted page table

## Slide 21: Virtual-To-Physical Lookup
Program only knows virtual addresses
  Each process goes from 0 to highest address
Each memory access must be translated
  Involves walk-through of (hierarchical) page tables
  Page table is in memory
    An extra memory access for each memory access???
Solution
  Cache part of page table (hierarchy) in fast associative memory – Translation-Lookahead-Buffer (TLB)
  Introduces TLB hits, misses etc.

## Slide 22: Translation Look-aside Buffer (TLB)
offset
Virtual address
.
.
.
PPage#
...
PPage#
...
PPage#
...
PPage #
offset
Physical address
VPage #
TLB
Hit
Miss
Real
page
table
VPage#
VPage#
VPage#

## Slide 23: Bits in A TLB Entry
Common (necessary) bits
  Virtual page number: match with the virtual address
  Physical page number: translated address
  Valid
  Access bits: kernel and user (nil, read, write)
Optional (useful) bits
  Process tag
  Reference
  Modify
  Cacheable

## Slide 24: Hardware-Controlled TLB
On a TLB miss
  Hardware loads the PTE into the TLB
    Need to write back if there is no free entry
  Generate a fault if the page containing the PTE is invalid
  VM software performs fault handling
  Restart the CPU
On a TLB hit, hardware checks the valid bit
  If valid, pointer to page frame in memory
  If invalid, the hardware generates a page fault
    Perform page fault handling
    Restart the faulting instruction

## Slide 25: Software-Controlled TLB
On a miss in TLB
  Write back if there is no free entry
  Check if the page containing the PTE is in memory
  If not, perform page fault handling
  Load the PTE into the TLB
  Restart the faulting instruction
On a hit in TLB, the hardware checks valid bit
  If valid, pointer to page frame in memory
  If invalid, the hardware generates a page fault
    Perform page fault handling
    Restart the faulting instruction

## Slide 26: Hardware vs. Software Controlled
Hardware approach
  Efficient
  Inflexible
  Need more space for page table
Software approach
  Flexible
  Software can do mappings by hashing
    PP#  (Pid, VP#)
    (Pid, VP#)  PP#
  Can deal with large virtual address space

## Slide 27: Cache vs. TLB
Similarity
  Both are fast and expensive with respect to capasity
  Both cache a portion of memory
  Both write back on a miss
Differences
  TLB is usually fully set-associative
  Cache can be direct-mapped
  TLB does not deal with consistency with memory
  TLB can be controlled by software
Logically TLB lookup appears ahead of cache lookup, careful design allows overlapped lookup
Combine L1 cache with TLB
  Virtually addressed cache
  Why wouldn’t everyone use virtually addressed cache?

## Slide 28: TLB Related Issues
What TLB entry to be replaced?
  Random
  Pseudo LRU
What happens on a context switch?
  Process tag: change TLB registers and process register
  No process tag: Invalidate the entire TLB contents
What happens when changing a page table entry?
  Change the entry in memory
  Invalidate the TLB entry

## Slide 29: Consistency Issue
Snoopy cache protocols
  Maintain cache consistency with DRAM, even when DMA happens
Consistency between DRAM and TLBs:
  You need to flush (SW) related TLBs whenever changing a page table entry in memory
Multiprocessors need TLB “shootdown”
  When you modify a page table entry, you need to do to flush (“shootdown”) all related TLB entries on every processor

## Slide 30: Summary
Virtual memory
  Easier SW development
  Better memory utilization
  Protection
Address translation
  Base & bound: Simple, but limited
  Segmentation: Useful but complex
Paging: Best tradeoff currently
  TLB: Fast translation
  VM needs to handle TLB consistency issues