## Slide 1: Changing picture brightness using SSE
Another SSE example….

## Slide 2: Brightness
Make a simple program that change the brightness of a picture by adding a brightness value between -128 and 127 to each pixel. A positive value makes the picture brighter, a negative value darker.
Assume it is a one byte pixel in gray scale, or a YUV picture where you operate on the Y-part only.
make_brighter

## Slide 3: Brightness – main
<.. includes ..>
int main (int argc, char *argv[])
{
< ... more variables ... >
unsigned char *bw_image;
int image_len, bright_value;
< open input and output files >
bright_value = atoi( argv[???] );
image_len = atoi( argv[???] ) * atoi( argv[???] ); /* picture width * picture height */
bw_image = (unsigned char *) malloc(image_len + 15); /* +15 to allow 16-byte alignment */
if ((((long)bw_image) % 16) != 0) bw_image += 16 - ((long)bw_image % 16); /* align */
< read picture to into memory with first pixel at "bw_image" >
if (bright_value !=0 ) brightness( bw_image, image_len, bright_value );
< write picture back to file >
< free memory, close descriptors >
}

## Slide 4: Brightness – Naïve C
void brightness (unsigned char *buffer, int len, int v)
{
int t, new_pixel_value;
if (v > 0) {
for (t = 0; t < len; t++) { /* make brighter */
new_pixel_value = buffer[t] + v;
if (new_pixel_value > 255) new_pixel_value = 255;
buffer[t] = new_pixel_value;
}
} else {
for (t = 0; t < len; t++) { /* make darker */
new_pixel_value = buffer[t] + v;
if (new_pixel_value < 0) new_pixel_value = 0;
buffer[t] = new_pixel_value;
}
}
}

## Slide 5: Brightness – SSE ASM
; void brightness_sse_asm(unsigned char *image, int len, int v)
brightness_sse_asm:
pushall
mov ebp, esp
mov edi, [ebp+12] ; unsigned char *image
mov ecx, [ebp+16] ; int len
mov eax, [ebp+20] ; int v in [-128, 127]
test eax, 0x80000000 ; check if v is negative
jz bright_not_neg
xor al, 255 ; make al abs(v)
inc al ; add 1
bright_not_neg:
shr ecx, 4 ; len = len / 16 (shift right 4)
mov ah, al ; xmm1=(v,v,v,v,v,v,v,v,v,v,v,v,v,v,v,v)
pinsrw xmm1, ax, 0 ; Packed Insert Word
pinsrw xmm1, ax, 1
pinsrw xmm1, ax, 2
pinsrw xmm1, ax, 3
pinsrw xmm1, ax, 4
pinsrw xmm1, ax, 5
pinsrw xmm1, ax, 6
pinsrw xmm1, ax, 7
test eax, 0xff000000 ; if v was negative,
jnz dark_loop ; make darker
bright_loop:
movdqa xmm0, [edi] ; move aligned double quadword
paddusb xmm0, xmm1 ; packed add unsigned
movdqa [edi], xmm0
add edi, 16 ; ptr = ptr + 16
loop bright_loop ; while (count>0)
jmp exit
dark_loop:
movdqa xmm0, [edi]
psubusb xmm0, xmm1
movdqa [edi], xmm0
add edi, 16 ; ptr=ptr+16
loop dark_loop ; while (count>0)
exit:
popall
ret
PINSRW (Packed Insert Word) moves the lower word in a 32-bit integer register or 16-bit word from memory into one of the four word locations in destination (MMX/SSE) register, selected by the two least significant bits of the immediate operand. The insertion is done in such a way that the three other words from the destination register are left untouched.
;; Less instructions ALTERNATIVE ;; using shufps
move ah, al
pinsrw xmm1, ax, 0
pinsrw xmm1, ax, 1
shufps xmm1, xmm1, 0x00
MOVDQA (move aligned double) Moves a double quadword from the source operand (second operand) to the destination operand (first operand).
PADDUSB (Packed Add Unsigned with Saturation) instruction adds packed unsigned byte integers. When an individual byte result is beyond the range of an unsigned byte integer (that is, greater than 0xFF), the saturated value of 0xFF is written to the destination operand.
PSUBUSB (Packed Subtract Unsigned with Saturation) instruction subtracts packed unsigned byte integers. When an individual byte result is less than zero (a negative value), the saturated value of 0x00 is written to the destination operand.

## Slide 6: Brightness – SSE Intrinsics
void brightness_sse_xscale (unsigned char *buffer, int len, int v)
{
__m128 pixel_vector;
__m128 value_vector;
int t;
if (v > 0) {
< make v char >
value_vector = _mm_set1_epi8( v ); /* PINSRW, SHUFPS, etc..*/
for (t = 0; t < len; t += 16) {
pixel_vector = (__int128 *)(buffer+t); /* MOVDQA */
pixel_vector = _mm_adds_epi8(pixel_vector, value_vector); /* PADDUSB */
*((__m128 *)(buffer+t)) = pixel_vector; /* MOVDQA */
}
} else { % (v <= 0)
v=-v;
< make v char >
value_vector = _mm_set1_epi8(v);
for (t = 0; t < len; t += 16) {
pixel_vector = (__int128 *)(buffer+t); /* MOVDQA */
pixel_vector = _mm_subs_epi8(pixel_vector, value_vector); /* PSUBUSB */
*((__m128 *)(buffer+t)) = pixel_vector; /* MOVDQA */
}
}
}
NB! Not tested…